## Slide 1
Mars Rover CDR
York Area Rocketry Team

## Slide 2: Presentation Overview
System Overview
  Mission Summary
  System Requirements
  System Level Concept Trade
  System Concept of Operations
  Physical Layout
Overview of Rocket
  Major Components Identified
  Rocket Weight
  Motor Selection
  Airframe Diameter
  Fin Size
  Number of Fins
  Length of Rocket
  CP and CG Identified

## Slide 3: Presentation Overview(Cont.)
Overview of Rocket (Cont.)
  Rocket Materials
Rocket Recovery System
  Parachute Selection
  Decent Rate
  Type of Shock Cord
  Linkages and Strengths
  Attachment Points to Frame
  Parachute of Selection
  Parachute Protection
Parachute Ejection
  Altimeter/Motor Ejection
Rocket Motor Selection
  Primary Motor Selection

## Slide 4: Presentation Overview(Cont.)
Rocket Motor Selection (Cont.)
  Primary Motor Thrust to Weight Ratio
  Secondary Motor
  Secondary Motor Thrust to Weight Ratio
  Primary Motor Flight Simulation
  Secondary Motor Flight Simulation
Rover Design
  Rover Design Overview, Rover Mechanics, Rover Materials, Rover Descent Control, Rover Mass
  Rover Electronics, Rover Camera, Rover Image Transmission
  Rover Image Transmission
  Rover Power, Rover Power Distribution
  Rover Markers
  Rover Software Design, Software Flowchart, Rover Payload Integration

## Slide 5: Presentation Overview(Cont.)
Rover Testing
  Subsystem testing
  Intergration Testing
  Functional Testing
Rocket Testing
  Parachute Deployment Testing
  Payload Deployment Testing
  Flight Testing
Flight Operations
  Rocket Prep
  Rover Prep
  Rover Intergration into Rocket
  Launch Pad Preparation
  Rover aiming process

## Slide 6: Presentation Overview(Cont.)
Program Schedule
  Gantt Chart
  Component and Service Schedule
Program Budget
  Rover Component
  Rocket Components
  Services
  Travel expenses
Summary

## Slide 7: Presentation Outline
Team Member Name | Section Presenting
Adam Winchell | Intro & Rocket Design
Zach Ruth | Rocket Design
Sarah Staley | System Overview
Ryan Shields | System Overview
Gabe Berman | Schedule
Jakub Becker | Rover Design
Michael Geyer | Rover Design
Tyler Sengia | Testing & Schedule
Hayden Forbush | Budgeting

## Slide 8: Team Organization
Team Member Name | Section Presenting
Adam Winchell | Intro & Rocket Design
Zach Ruth | Rocket Design
Sarah Staley | System Overview
Ryan Shields | System Overview
Gabe Berman | Schedule
Jakub Becker | Rover Design
Michael Geyer | Rover Design
Tyler Sengia | Testing & Schedule
Hayden Forbush | Budgeting
Team Member Name & Grade | Team Member Role
Adam Winchell – 12 | Team Captain
Zachary Ruth – 12 | Team Co-Captain
Tyler Sengia -12 | Rover Software Developer
Michael Geyer -12 | Rover Hardware Developer
Ryan Shields -12 | System Developer
Jakub Becker – 11 | Rover Manufacturing
Sarah Staley – 11 | Electronics Bay Developer
Gabriel Berman -11 | Team Safety Officer
Hayden Forbush -9 | Financial Scheduler

## Slide 9: Acronyms
PDR: Preliminary design review
CDR: Critical design review
CONOPS: Concept of operations
CP: Center of pressure
CG: Center of Gravity
MDRA- Maryland-Delaware Rocketry Association
TWR – Thrust to Weight Ratio
UTS – Ultrasonic Sensor
ICST – Image Capture Storage and Transmission
TANK – Treaded Automated Navigational Kit

## Slide 10
System Overview

## Slide 11: Mission Summary
Design a rocket and Mars rover to launch to at least 1000 feet and deploy the Mars rover. The Mars rover must be fully contained in the rocket before being deployed. Once deployed, the Mars rover must return to the ground safely. When it lands, the rover will take a picture with a camera. Up to four images will be taken, each image in the forward, left, right, and rear direction. Afterwards, the Mars rover shall release a bright colored marker that can be easily found. The marker must be placed at the point of landing. It cannot be tossed, shot, or projected beyond its landing location. Once released, the rover must then travel 10 feet and release a second marker. The rover then must turn or move 90 degrees in either direction and travel 10 feet. Travel must be completed within ten minutes. Time starts at the time of landing. Method of travel is up to the team.

## Slide 12: System Requirement Summary Rover
Rover must weigh less than 2 Kg completely within the rocket while working autonomously
Rover recovery system must be secure and no pyrotechnics are allowed
4 pictures will be taken in color at 640x480 or higher
At landing, the rover must release the recovery system
Must travel 10 feet or 120 inches then drop a marker
Travel a minimum of two feet in each segment
The rover must be able to detect when it has flown and landed
Travel must be completed within 10 minutes of landing

## Slide 13: System Requirement Summary Rocket
Total installed impulse shall not exceed 2,560 Newton-seconds or a K motor
All parts of the rocket must safely return under a recovery system
The airframe, nose cone, fins, bulk plates, and centering rings cannot be made of any types of metal
The rocket must reach at least 1000 feet
Must use a commercial altimeter
Average TWR must be greater than 5:1
The rocket must use a motor retainer

## Slide 14: System Concept of Operations Rover
Provide overview of operations of the system from launch to landing to rover operations.
  Launch and descent operations
  Rover Operations
    Ultrasonic Sensor detects when to release parachute from lander
    Lander makes contact, arms extend, and lander is righted if landed on side
    Cameras takes pictures and write them to SD cards
    Tank protocol begins, and tank drives out of lander
    Pictures are relayed to ground station
    Tank stops at 10 ft, moves turret to release marker, turns and continues
  Post-launch recovery
Simple flow diagrams and cartoons are a good way to present the CONOPS

## Slide 15: System Level Concept
“Rover”
Lander
“Tank”
Structure
Electronics
Communication
Deployment Subsystem
Parachute Subsystem
Structure
Electronics
Marker
Deployment
Notes: Present final system level concept of the rocket and rover.
This is an overview of what will be shown later in greater detail
Identify major parts

## Slide 16: Physical Layout

## Slide 17: Physical Layout cont.

## Slide 18: Physical Layout cont.

## Slide 19: System Concept of Operations Rocket
Overview of operations of the system from launch to landing to Payload operations.

## Slide 20: Post Launch Recovery
Safety officer and team adviser will go out to retrieve the rocket.
They will use the tracking receivers in order to locate the rocket sections.
The electronics will be disarmed using the “Remove Before Flight” keys, and the black powder charges will be checked by the team advisor for any possible dangers.
The rocket will then be deemed safe to carry, and transport back to base of operations.

## Slide 21: Physical Layout of Rocket
Diagram of rocket showing major components
  The rocket will be 141 inches long, and have a 12 inch diameter body tube.
  The rover will be located in the front half of the body tube, along with the main parachute while the drogue chute will be in the back half of the body tube.
  The E-Bay will be setting off an ejection charge. This charge will blow off the nosecone, causing it to pull the rover in the sabot out of the front boy tube.
Rover
E-Bay
Nose cone
Front body tube
Back body tube
Fins

## Slide 22: Physical Layout of Rover
Diagram of rover
  H: 355mm W: 280mm L: 280mm
  Major Components
    tank - Free from lander, flying during maneuvers
    tank Controller - Housed in lander, controlled by Arduino
    Arduino - Housed in Lander, main interface for components
    Ultrasonic Sensor - Housed in cutout in bottom of lander, senses ground approaching to signal release of parachute
    Camera - Housed on top of lander
    Base station - Kept at launch site, used to recover pictures wirelessly

## Slide 23
Rocket Design

## Slide 24: Changes Since PDR - Rocket
  The material used for the body tubes has been changed to phenolic tubing to decrease mass of the rocket and to obtain a TWR of at least 5:1
  Fin design has been changed to move Center of Pressure back, increasing stability and reducing the mass as well.
  The new motor selected is a Cesaroni K1440 White Thunder. This motor will get our redesigned rocket to the target altitude, and it meets the 5:1 TWR requirement

## Slide 25: Changes Since PDR - Rover

## Slide 26: Overview of Rocket
Describe overall rocket design
  Nose cone connected to front body tube, which is connected to the electronics bay, serving as a tube coupler between the front and back body tubes. Fins are attached to the back body tube, and the motor tube is inserted and mounted inside the back body tube
  Total Weight – 52.70 lbs.
  Motor - Cesaroni K1440
  Diameter – 12”
  The rocket is built with
  a three-fin-design.
  141.13 inches (11 ft. 9 in.)
  CG is 79.94 inches from the front end and CP is 101.14 inches. This is 21.2 inches apart, and based on the diameter of the rocket, this gives a margin of 1.86.

## Slide 27: Rocket Materials
Airframe Material - 1/8 inch Phenolic Tubing
Fin Material - 1/8 inch fiberglass fins
Nosecone material – Fiberglass
Adhesives Used - Rocket-Poxy, 5-Minute Epoxy, and JB Weld. They were all used for centering ring and fin attachment
Rail Guides - Unistrut Rail Buttons
Active Motor Retention using Aeropack Motor Retainer

## Slide 28: Rocket Recovery System
Parachute selection- 10 ft Iris Ultra parachute from Fruity Chutes for main parachute, and 72 inch elliptical for drogue parachute
Descent Rate Under main- 17.26 ft/s
Descent Rate Under drogue- 26.16 ft/s
Harnesses
  7/16 inch tubular Kevlar, 25 feet long for front, and 25 feet for back half
  Swivel to hold parachute using quick links. 880 lbs. max
  Quick links attached to parachutes are attached to the swivel on the shock cord which are secured to U-Bolts on the rocket using quick links
  Parachutes are protected by Nomex heat shields, and Nomex sleeves are put on the shock cord for protection

## Slide 29: Rocket Recovery System Deployment Method
Altimeter used will be a PerfectFlite Stratologger CF. Ejection charges will be at apogee and 600 feet above the ground. It will be Altimeter-Based Ejections (Primary and Secondary)
  When loading, an 18 year old student holds electronics bay, while the NAR mentor loads and seals the black powder ejection wells.
  To arm the recovery system, while on the pad, key switches are turned arming the altimeter. Key switches are removed and stored with the recovery team.
  Key switches are turned arming the recovery system before the igniter is inserted to ensure safety in the case of an accidental launch.
Through online calculation and experience, we will be using 9.6 g of 4F grain size black powder for the front and back half to obtain an ejection pressure of 14 psi. We will testing extensively in ground ejection tests in order to get an exact desired and safe number.

## Slide 30: Wiring diagram of altimeter
9V Battery
9V Battery
Altimeter
Altimeter
To Main
To Main
To Drogue
To Drogue
To Key Switches

## Slide 31: Wiring diagram of altimeter
Altimeter
Altimeter
Main Primary
Main Secondary
Drogue Primary
Drogue Secondary

## Slide 32: Rocket Motor Selection
Primary motor selection – Aerotech K1440 (6.1 : 1 TWR)
Secondary motor selection – Ceseroni K2000 VMAX (8.5 : 1 TWR)
RockSim 9 was used for all simulations

## Slide 33: Test Flights
Show results of any test flights
  There have been no test flights yet, as our January launch was canceled due to weather. We plan to have a launch on February 17 and 18 and one also in March if needed.

## Slide 34
Rover Design

## Slide 35: Rover Design Overview

## Slide 36: Rover Design Overview cont.

## Slide 37: Rover Design Overview cont.

## Slide 38
Mechanical Subsystem

## Slide 39: Mechanical Layout
Show Mechanical Layout of rover
  Show structure of rover
  Identify location of major components
  Identify major mechanical parts

## Slide 40: Mechanical Layout

## Slide 41: Rover Descent Control

## Slide 42: Rover Mass Budget
Rover Mass Budget |  |  | 
Component | Mass (g) | total mass (g) | Uncertainty
Panels (x5) | 30.9 | 154.5 | 10
Motor | 138.5 | 138.5 | 0.1
3D printed components | 500 | 500 | 50
Electronics | 290 | 290 | 20
Power Systems | 105 | 105 | 10
TANK | 158 | 158 | 20
TOTALS: |  | 1346 | 110.1

## Slide 43
Rover Electronics

## Slide 44
Block Diagram
Arduino
Parachute Separation
Power Source
Arming Button
Tank Deployment/
Unfolding Mechanism
Tank
Tank Controller
Alt. Power Source
Ultrasonic Sensor
Accelerometer
XBee
SD Card Reader

## Slide 45: Rover Electronics

## Slide 46: Processor and Memory
●Arduino Mega
−ATmega2560, 256 kB flash, 8 kB SRAM, 4 kB EEPROM
−Operating Voltage: 5V, Input Voltage: 9V
−Processor Speed: 16 MHz
−54 digital IO pins, 16 analog input pins

## Slide 47: Rover Sensors
  ●Identify sensors to be used to determine state of rover
  −Ultrasonic Sensor (MB1040)
  Range: 15-640cm
  Working Voltage and Amperage: 5V, 2.0mA
  −Accelerometer (MMA8541)
  Resolution: 14 bit
  Working Voltage and Amperage: 1.95V-3.6V, 6μA-165μA
  8 pins to Arduino

## Slide 48: Rover Camera

## Slide 49: Rover Image Transmission

## Slide 50: Image Transmission Trade (cont.)

## Slide 51: Rover Power
Lander
  5 NiMH AA Batteries (7.5V), total of 1,200 to 1,900 mAh
  Mechanical Box Encasement
  Rechargeable, sufficient power, cost effective
  Protection circuits
    Arduino - Reverse Polarity Detection/Short Circuit Protection
Tank
  2 NiMH AA Batteries

## Slide 52: Lander Power Distribution
Lander Electrical Power System Design
  Arduino Built-in 5 Volt, 1 Amp Regulator (NCP1117ST50T3G)
  Jumper cables for distribution to sensors

## Slide 53
Software

## Slide 54: Lander Software Design
Software States:
1. Pre-Mission Idle
2. Armed
3. Descent
4. ICST
5. Tank Command
6. Post-Mission Idle

## Slide 55: Telemetry

## Slide 56: Software Flow Chart
START
Battery
connected
Pre-Mission Idle State
Waiting for “ARM” command to be received from XBee
Armed State
Waiting for large downwards acceleration
Descent State
Waiting for distance to ground to measure 10 feet (UTS)
Motor releases parachute
30 second Delay
ICST
State
Images Captured and Stored
Images Transmitted
Tank
Command State
Tank is Driven by Lander
Post-Mission Idle State

## Slide 57: Software Development Plan
Software Development Plan
The purpose of this system is to control the arming of the Lander, release of the parachute from the Lander, the sensing of impact with ground, the capture, storage, and transmission of 4 images, and the deployment and navigation of the Tank.
This software applies to the Arduino MEGA 256 that is on the Lander.
Software is used in tandem with the 2018 York Area Mars Rover Team Ground Station Program which sends the arming signal and processes the images.

## Slide 58: Software Development Plan (cont)

## Slide 59: Rover Payload Integration
Foam Sabot
Describe process of payload integration
  Rover is turned on, in the Software “Pre-Mission Idle” State, and placed in the sabot which is then placed in the rocket.

## Slide 60: Software Development Plan (cont.)

## Slide 61: Software Development Plan (cont)
Ground Station GUI
Python 3.5 program
Utilizes: PySerial, GTK3
GUI designed using Glade
Communicates over serial to the XBee, which then transmits to the Rover XBee
Saves Images received from Rover
Keeps logs of outgoing and incoming data
Can send commands
ARM - Sets the Rover’s software state to the “Armed” State
KILL - Legacy command for previous tank concept (remote kill switch)
Test Commands
“TEST1” - Test of ICST
Test Connection - Sends out “pings” to the Rover and waits for replies. Test connection quality.

## Slide 62
Testing

## Slide 63: Rover Testing
Subsystem Testing
●Image capture and saving to SD card
●Serial communication over Lander XBee to Ground Station XBee
Integration Testing
●Pre-launch Test Program to check sensors and electronics
Functional Testing
●Programmed Tank Paths
○The Tank path programs are adjusted from test to test to find the best travel path
●Test flight will be done to test if Launch, Descent, and Landing accelerations are recognized/detected
●Test flight to test if proximity to ground is detected accurately

## Slide 64: Rocket Testing
Ejection charge test on December 17
  One of the bulk heads was damaged on the electronics bay, our design had to be altered
Dec 19 through Jan 16 – Ebay was strengthened by adding two plywood rings and wooden joists separating them. The bulkheads rest and seal against the wooden ring.
Flight test planned for January 13 and 14, cancelled due to weather
Jan 26 – Ejection charges were tested by attaching the rocket to a zipline. Videos to follow.
Next flight test planned for February 17 and 18

## Slide 65: Ejection Charge Test (Drogue)

## Slide 66: Ejection Charge Test (Main)

## Slide 67: Flight Operations
  The rocket will have new batteries in the E-Bay before every launch, and before the launch, all altimeters will be tested.
  Freshly charged batteries are put in tank and Lander
    Test Program is uploaded to Lander to check sensors/connections
  The rover will be incorporated into the rocket by being inside a sabot
  At the launch pad, the key switches will be turned and arm the electronics bay.
  After Rover is placed in payload section:
    Arming Button is pressed and prep cycle commences

## Slide 68: Rocket Program Schedule

## Slide 69: Payload Program Schedule

## Slide 70: Rocket Program Schedule

## Slide 71: Service and Component Schedule
The rockets components were all received on November 17 2017
K-1000 motors were ordered on October 30th, and arrived January 5th
K-1440 motors were ordered January 16 and arrived January 24
Parachutes were ordered October 20th, and arrived December 11th
Phenolic Body tubes were ordered from Public Missiles limited on December 13th and received them December 20th
The body tubes were precut by the company at about the time it was ordered.

## Slide 72: Program Budget
Components

## Slide 73: Program Budget
Services

## Slide 74: Program Budget
Travel expenses
Grand Total

## Slide 75: Program budget cont.

## Slide 76: Payload Summary
Development moves very fast, every day new ideas arise and changes/additions are made to the design. Some key accomplishments were successfully transmitting images and successful sensor testing. Some issues we ran into were the legality of our “rover”, material requirements, sensor accuracy, and lander layout. The electronics system is in the process of being constructed into its final form, and the lander and rover designs are beginning to be constructed.

## Slide 77: Rocket Summary
Now we are reconstructing the rocket and so far redesigning the rocket has gone well. It's design so the rocket is lighter, fixing the issue with the CG and the CP. We fixed this issue by enlarging the fins so the CP is behind the CG by at least by a caliber. we are almost complete with making the rocket lighter to fix the 5:1 TWR. Thus far the only tests that have been completed on the rocket is an ejection test that was successful but the first flight is scheduled to happen on our pending February launch.