## Slide 1: Mars Rover Rocket Safety Document
Spring Grove Area High School &
Dover Area High School
York Area Rocketry Team

## Slide 2: Rocket Design
Airframe Material - 1/8 inch Phenolic Tubing
Fin Material – 1/8 inch fiberglass fins
Nosecone material – Fiberglass
Adhesives Used - Rocket-Poxy, 5-Minute Epoxy, and JB Weld.
Rail Guides - Unistrut Rail Buttons
Bulkheads – 1/2 inch plywood
Motor Tube – 1/8 inch Phenolic Tubing
Parachute selection- 10 ft Iris Ultra parachute from Fruity Chutes for main parachute, and 72 inch elliptical for drogue parachute. They’re protected by Nomex heat shields and Nomex shock cord sleeves.
7/16 inch tubular Kevlar (50 feet)
880 lb. limit quick links and swivels
Key Switch - Type 2, made by CNK
U Bolts
Wires
Ejection Wells – 1” PVC caps
Notes: http://www.nar.org/nar-products/rocket-stability/

## Slide 3: Rocket Design
A drawing of the rocket identifying all of its components and their dimensions
Rover
Main Chute
Drogue
Chute
Motor
Nose Cone:
Front Body Tube:
Back Body Tube:
Motor: 22.4 in
Rover:
Full Rocket: 141.14 in.
Notes: http://www.nar.org/nar-products/rocket-stability/

## Slide 4: Rocket Design (cont.)
Total on the pad weight of rocket
  With Primary Motor: 52.70 lbs
  With Secondary Motor: 53.96 lbs
Location of Center of Pressure (CP) from the tip of the nose cone
  101.14 inches
Location of Center of Gravity (CG) from the tip of the nose
  With Primary motor: 79.92 inches
  With Backup motor: 81.43 inches
Stability Margins
  With Primary motor: 1.86
  With Backup motor: 1.73
Notes: http://www.nar.org/nar-products/rocket-stability/

## Slide 5: Primary and Secondary Motors
Primary motor selection – Aerotech K1440
It will be using active motor retention with an Aeropack Motor Retainer
TWR = 6.2:1 (on pad with motor and using average thrust of motor)
Secondary motor selection – Cesaroni 2000 VMAX
It will be using active motor retention with an Aeropack Motor Retainer
TWR = 8.6:1 (on pad with motor and using average thrust of motor)

## Slide 6: Recovery
Document method of initiating recovery
  Electronics Bay is used for ejection charge initiations.
Parachute
  10 ft Iris Ultra parachute from Fruity Chutes for main parachute, and 72 inch elliptical for drogue parachute
  The drogue is as large as it is to reduce the decent rate enough for the rover to be able to deploy safely.
  For main, a safe decent is less than 20ft/s. We used RockSim to calculate the decent rate.
  To protect the parachutes, Nomex deployment bags will be used.

## Slide 7: Recovery
  7/16 inch tubular Kevlar, 1200 lb. max
  Swivel and quick links. 880 lbs. max
  U-Bolts are mounted to the E-bay bulkheads with washers and lock nuts, and then epoxy overtop. This stops the nuts from coming loose, or anything un-attaching
Rover
Main Chute
Drogue
Chute

## Slide 8: Recovery Electronics
Identify commercial altimeter(s) that will be used
  Stratologger CF from PerfectFlite
Show wiring diagram of altimeters with charges
Altimeter
Altimeter
Main Primary
Main Secondary
Drogue Primary
Drogue Secondary

## Slide 9: Recovery Electronics
Three ½ inch portholes were drilled
The altimeter will be prepared by replacing batteries within an hour before launch, and testing continuity.
Drogue – 13 grams of black powder was tested and was successful
Main – 7 grams of black powder was tested and was successful
Specify the volume of the section to be pressurized with calculated pressure level
Drogue – 3607 in^2
Main – 1973 in^2
Specify how sections are secured before the ejection charges separate sections
  shear pins – 0.075” (x3)
Identify how charges are fired
  e-matches